## Slide 1: The ITER ICRF system under the new ITER baseline: latest updates and technological developments
W. Helou, F. Calarco, N. Ferrigno, F. Kazarian, K. Saito, V. Bobkov, L. Colas, P. Dumortier, F. Durodié, E. Lerche, R. Maggiora, D. Milanesio, S. Porporato, S. Salvador, M. Schneider, R. Anand, J. Appanam Karakkad, H. Aubert, C. Barbier, P. Barges, B. Beaumont, M. Bécoulet, J.-M. Bernard, N. Bertelli, A. Bustos, A. Cadinot, H. Faugel, N. Faure, R. Goulding, M. Graham, D. Guillermain, J. Hillairet, P. Jacquet, J. Jacquinot, A. Jha, A. Kaye, F. Koechl, A. Krivska, A. Kumar, R. Kumar, P. Lamalle, A. Loarte, G. Lombard, F. Louche, V. Maquet, I. Minondo, P. Mollard, I. Monakhov, A. Mukherjee, J. Myra, R. Ochoukov, A. Patel, M. Patel, R. Pitts, C. Qin, S. Shiraiwa, R. Singh, G. Suthar, W. Tierens, R. Trivedi, G. Urbanczyk, M. Usoltseva, D. Van Eester, Y. Wang, T. Wauters, Z. Wolfe, H. Yang, W. Zhang, and X. Zhang.
Disclaimer: The views and opinions expressed herein do not necessarily reflect those of the ITER Organization

## Slide 2: Acknowledgments

## Slide 3: Outline
ITER ICRF system under the new ITER Research Plan (IRP).
ICRH scenarios.
Ion Cyclotron Wall Conditioning (ICWC).
Coupling and local gas injection modelling.
ICRF specific sputtering predictions under W-wall.
Full system RF modelling.
Antenna RF and mechanical design activities.
Antenna protections and arc detection.
Prototyping activities.
Conclusion and timeline.

## Slide 4: Outline
ITER ICRF system under the new ITER Research Plan (IRP).
ICRH scenarios.
Ion Cyclotron Wall Conditioning (ICWC).
Coupling and local gas injection modelling.
ICRF specific sputtering predictions under W-wall.
Full system RF modelling.
Antenna RF and mechanical design activities.
Antenna protections and arc detection.
Prototyping activities.
Conclusion and timeline.

## Slide 5: Outline
ITER ICRF system under the new ITER Research Plan (IRP).
ICRH scenarios.
Ion Cyclotron Wall Conditioning (ICWC).
Coupling and local gas injection modelling.
ICRF specific sputtering predictions under W-wall.
Full system RF modelling.
Antenna RF and mechanical design activities.
Antenna protections and arc detection.
Prototyping activities.
Conclusion and timeline.

## Slide 6: Heating & Current Drive (HCD) under the new IRP
New baseline: change of First Wall material from Be to W.
Modified Heating and Current Drive (H&CD) strategy:​
[M. Schneider, et al., this conf.]
Electron Cyclotron Heating (ECH) increased by factor 2-3 (40-67 MW​).
Ion Cyclotron Heating (ICH) set to 10-20 MW​.
10 MW for the Start of Research Operation (SRO) for ICWC and tests of ICH under high-Z wall.
Rationale behind the new H&CD mix:​
Dominant ECH to overcome the increased W source.
More H&CD power to reduce need for fusion alphas in development path to Q=10 (limited neutron budget in DT-1)​.

## Slide 7: Basis of the new HCD level and mix
# | Task / Target | Heating mix consideration
1 | Enable H-mode operation in SRO. | 40 MW of ECRH.
2 | ICRH operation in full W wall: tests of ICRH coupling & ICRF-specific sputtering. | 10 MW ICRF system to be experimentally validated in SRO before any upgrade to 20 MW for DT-1.
3 | Tests of fuel removal in SRO (ICWC). | 
4 | Enable DD H-mode development to high Ip in DT-1. | 33 MW NBI. 60-67 MW ECRH.
5 | Enable access to high Q for Prad/Ptot > 0.3. | 
6 | Enable Q=5 steady state operation for DT-2. | HNB-3.

## Slide 8: HCD mix in SRO, DT-1 and DT-2
ICRF upgrade to 20 MW
ICRF power of 10MW in SRO
HNB installed power of 33MW
ECRF installed power of 40MW in SRO
ECRF installed power of 60MW in DT-1
ECRF upgrade up to 67MW
HNB3 upgrade

## Slide 9: Scenario development pathway in SRO and DT-1
Use of W wall favours BT values that provide effective central heating.
 Scenario development at 2.65 and 5.3 T.
 | SRO |  | DT-1 | 
ECRF | 40 MW | 2.65 T X2 in L-mode, O2 in H-mode. | 60-67 MW | 2.65 T X2 in L-mode, O2 in H-mode.
 |  | 5.30 T O1. |  | 5.30 T O1.
ICRF | 10 MW | 2.65 T In D at ~42 MHz: H minority (N=1), or, D majority (N=2). In H: No efficient scheme. | 10-20 MW | 2.65 T In D and DT at ~42 MHz: H minority (N=1), or, D majority (N=2). in H: No efficient scheme.
 |  | 5.30 T In D or H at ~53 MHz: 3He minority (N=1). |  | 5.30 T In D or H at ~53 MHz: 3He minority (N=1). In DT at ~53 MHz: 3He minority (N=1), T majority (N=2).
NBI |  |  | 33 MW | Up to 0.87 MeV H beams. Up to 1.00 MeV D beams.
Assess coupling & ICRF-specific sputtering.

## Slide 10: ITER ICRF system under the new IRP
2016 baseline
ICWC/ICRH with 10MW for SRO:
No technical requirements modified for the individual components of the ICRF system.
New location for the RF sources & HVPS (B15N allocated to ECRF).
1 antenna (instead of 2, second port allocated to ECRF).
The system is compatible with ICWC (needing 2-2.5 MW coupled to plasma  5 MW installed). 10 MW installed power relaxes constraints on ICWC and allows proper testing of ICRH.
The system is upgradable to 20 MW.
8+1 RF sources
and their HVPS
8 Transmission Lines
2 antennas
4 RF sources and their HVPS
4 Transmission Lines
1 antenna
2024 baseline for SRO
2.5 MW @ VSWR 2:1, 35-65 MHz, CW
3.0 MW @ VSWR 1.5:1, 40-55 MHz, CW

## Slide 11
Strap
Faraday Screen
Four Port Junction
Service T-stub
Front Window
(double barrier)
3.5 m × 2.0 m × 1.5 m, 45 tons.
24 straps array grouped in 8 triplets.
8 inputs. Flexibility for antenna array excitation.
4 RF modules.
Vacuum Transmission Line (oblong shaped)
The ITER ICRF antenna
Rear Window
45 kV peak nominal voltage.
Emax=2-3 kV/mm (depending on direction, and location).
Optimized for 40-55 MHz.
10 MW CW, compatible with 20 MW CW.
RF modules designed to maximize coupled power + provide neutron shielding and compliance to multiphysics requirements.
ATLIS (6 bar dry air)

## Slide 12: Outline
ITER ICRF system under the new ITER Research Plan (IRP).
ICRH scenarios.
Ion Cyclotron Wall Conditioning (ICWC).
Coupling and local gas injection modelling.
ICRF specific sputtering predictions under W-wall.
Full system RF modelling.
Antenna RF and mechanical design activities.
Antenna protections and arc detection.
Prototyping activities.
Conclusion and timeline.
Acknowledgments: M. Schneider, E. Lerche, F. Koechl, et al.
[E. Lerche, et al., this conf.]

## Slide 13: Effect of ICH on fusion performance
Waveforms of H&CD power and plasma density to access Q ~ 10 conditions for a range of H&CD mixes (assuming Prad = 30%):
For each case: the temporal evolution of density corresponds to the fastest density rise to achieve Q=10 (if too fast  H-L transition  Ti drops  Pα drops).
Slower density rise with only ECH).
Faster access to burning plasma conditions and increased fusion power with direct ion heating (NBI and ICH).
Such scenarios can be tested end of DT-1 or in DT-2.
Shot=53301, Runs 80 to 84.
[A. Loarte et al., “The new ITER Baseline, Research Plan and open R&D issues”, accepted to PPCF (2025)]

## Slide 14: SRO: Ion heating in D plasmas with ICH [1/2]
0.3%H
(residual)
2%H
On-axis H min. (2.65T/42MHz)
Off-axis H min. (2.65T/40MHz)
Bulk ion heating with H min. ICRH can be obtained by:
- Shifting the resonance off-axis (reducing the frequency).
- No H2 injection to enhance ω=2ωc D absorption.

## Slide 15
ICRH=10MW
ICRH=20MW
ICRH=0 (ref.)
ICRH increases Ti efficiently.
Ti>Te regime not reached with ECRH = 25MW; could require more than 20 MW ICRH or reducing ECRH power.
Ti <~ Te
Best ICRF settings for ion heating at 2.65T (L-mode):
ne0=4.7x1019/m3, Te0=12keV, Ti0=8keV
ECRH=25MW
SRO: Ion heating in D plasmas with ICH [2/2]

## Slide 16: D-T: Effect of ICH power on fusion performance [1/2]
0MW
8MW
20MW
30MW
ICRH: 3He / T heating in D-T H-mode plasmas (5.3 T / 15MA) - simpletransp
ΔTi = 5keV
ΔPfus = 200MW
ICRH can have a strong impact on Ti and on fusion power but 10 MW can be marginal.
For 20MW: ΔTi=4keV, ΔPfus=120MW

## Slide 17: D-T: Effect of ICH power on fusion performance [2/2]
Very clear effect on Q but then this saturates because ion temperature gradient hits stiffness limits and fusion power doses not go up much more with more ion heating.
Will be complemented by:
Scan extension to 40 MW of ICH, also case with 50 MW ECH and 40 MW ICH for comparison.

## Slide 18: High ICH power key for stationarity in seeded plasmas
Same behaviour is observed in JET Ar and Ne seeded plasmas.

## Slide 19: Outline
ITER ICRF system under the new ITER Research Plan (IRP).
ICRH scenarios.
Ion Cyclotron Wall Conditioning (ICWC).
Coupling and local gas injection modelling.
ICRF specific sputtering predictions under W-wall.
Full system RF modelling.
Antenna RF and mechanical design activities.
Antenna protections and arc detection.
Prototyping activities.
Conclusion and timeline.
Acknowledgments:
T. Wauters, et al.

## Slide 20: ICWC [1/2]
Uniform CXN flux of 6 – 8 x1018 D m-2s-1 in 0.1 - 1 keV range, based on:
  TOMAS and TORE SUPRA fluxes scaled to ITER power / surface area.
  Recent EAST LENPA data at ITER relevant power / surface area.
20 to 30 min ICWC in ITER (PICWC ~2 MW) at 15% duty cycle sufficient to deplete near surface layers of W and B, for effective plasma isotope control.
EAST joint exp. 2024
High implantation energy while maintaining long mean free path for CXN collisions to obtain a toroidally uniform flux

## Slide 21: ICWC [2/2]
Ionization by electrons accelerated by the parallel RF electric field (near ICRF antenna.
PIC-MCC model identified different phases in the density build-up from vacuum to slow wave cut-off.
Vacuum electric field
Plasma-generated electrostatic field
Plasma density evolution by Rfdinity-1D:
Challenges for ITER ICRF breakdown:
Antenna launches mainly E⊥.
ITER ICRF at 40-55 MHz, but breakdown suspected to be easier at low frequency (TBC).
Large torus circumference C: ionization rate (∝ 1/C).
f = 29 MHz, pH2 = 4×10-4 mbar, ASDEX Upgrade sized device
[Tripsky, et al., NF 2017]

## Slide 22: IC breakdown phase
|E//| > 8 kV/m at spots with at least ~50mm spatial extensions inside the first limited field line.
FS CMM
Modelled |E//| in vacuum, 45 kV peak, 40 MHz, monopole
Criterion fulfilled but verification needed in 3D Monte Carlo simulation.
Required field for IC breakdown @ 40 MHz in ITER, based on 1D simulation:
100 mm
[V/m]
[V/m]

## Slide 23: Steady ICH phase [1/3]
Uniform discharge produced by non-resonant damping on ions and electrons. Coupling resistance and radial expansion result from appearance of LHR.
Tomator-1D/KIPT-RF
2 antennas
In monopole
LHR
2.0-2.5 MW coupled to plasma (volumetric power scaling from JET with 100-200 kW). At 40-50% efficiency  5 MW source power.
Volume [m3]
Pcoupled [kW]

## Slide 24: Steady ICH phase [2/3]
Decreasing cut off density for fast wave propagation improves RF coupling and discharge homogeneity  Monopole (note: cavity mode at ~47.5 MHz).
Best coupling expected for [0;0;0;0] phasing
RF cavity in red
[0;0;φ;φ] phasing, with φ ≠ π.
[F. Louche, et al., this conf.]
[A. Krivska, et al. this conf.]

## Slide 25: Steady ICH phase [3/3]
3 ICWC density profiles for sensitivity analysis
ICWC LOW | [0;0;0;0] | [0;0;+π/2;+π/2] | [0;0;π;π]
40 MHz | 40.2 kV / 2.0 MW | 45.0 kV / 1.4 MW | 45 kV / 0.2 MW
53 MHz | 22.5 kV / 2.0 MW | 30.5 kV / 2.0 MW | 45 kV / 0.7 MW
ICWC Interm. | [0;0;0;0] | [0;0;+π/2;+π/2] | [0;0;π;π]
40 MHz | 30.6 kV / 2.0 MW | 41.5 kV / 2.0 MW | 45 kV / 0.4 MW
53 MHz | 16.7 kV / 2.0 MW | 22.4 kV / 2.0 MW | 45 kV / 1.6 MW
ICWC High | [0;0;0;0] | [0;0;+π/2;+π/2] | [0;0;π;π]
40 MHz | 8.9 kV / 2.0 MW | 11.4 kV / 2.0 MW | 19.5 kV / 2.0 MW
53 MHz | 3.7 kV / 2.0 MW | 4.6 kV / 2.0 MW | 6.4 kV / 2.0 MW
Color code
OK, OK
0.5 MW < PICWC < 1 MW
PICWC < 0.5 MW
For most cases, the antenna can deliver the required power for ICWC.
Straps
Wall
ANTITER IV modelling (Fast and Slow Waves) :
High.
Intermediate.
Low.

## Slide 26: Outline
ITER ICRF system under the new ITER Research Plan (IRP).
ICRH scenarios.
Ion Cyclotron Wall Conditioning (ICWC).
Coupling and local gas injection modelling.
ICRF specific sputtering predictions under W-wall.
Full system RF modelling.
Antenna RF and mechanical design activities.
Antenna protections and arc detection.
Prototyping activities.
Conclusion and timeline.

## Slide 27: Thorough RF coupling modelling
TOPICA
COMSOL(RAPLICASOL)
Petra-M
Examples:
Modelling in: TOPICA, COMSOL (RAPLICASOL), Petra-M, HFSS, MWS, ANTITER II & IV.
Benchmarks essential as per Quality Assurance.
Served for solid demonstration of system RF design, gas injection performance, operation strategies (optimized excitations, etc.), coupling capabilities, etc.
[Milanesio, et al., RFPPC 2022]
[Bertelli, et al., RFPPC 2022]
[Milanesio, et al., NF 2023]

## Slide 28: Variety of detailed CAD models
Several antenna versions, with/without surrounding port/plug cavity, with/without Four Port Junctions, etc.
Recently, comparisons with / without Faraday Screen
[Milanesio, et al., RFPPC 2022]
[Milanesio, et al., NF 2023]

## Slide 29: Robust benchmarks
Agreement on coupled power, E-fields, S & Z matrices, etc.
TOPICA
COMSOL

## Slide 30: Modelling for local gas injection with validated tools
Modelling using EMC3-EIRENE, following by RF coupling modelling (ATT II, ATT IV, TOPICA, COMSOL, Petra-M).
[W. Zhang, et al, NF 2023]
For all scenarios, local GI moves cut-off density towards the antenna by several cm.
Straps

## Slide 31: Boosting the coupling with local gas injection
Chart: 
| Divertor, P13 | Divertor, P15 | Top, P13 | Top, P15 | Local ICRF, P13 | Local ICRF, P15
[0;π;π;0] | 13.2527 | 12.9931 | 19.1111 | 33.2514 | 48.4383 | 50.8335
Power (MW)
×3
# | Divertor [1022 el/s] | Mid P13 [1022 el/s] | Mid P15 [1022 el/s] | Total [1022 el/s]
1 | 4.55 | 0 | 0 | 4.55
2 | 0 | 0.5625 | 0.5625 | 1.125
3 | 0 | 1.125 | 1.125 | 2.25
4 | 0 | 2.275 | 2.275 | 4.55
[W. Zhang, et al, NF 2023]

## Slide 32: Step forward in modelling capabilities
Example: modelling with 3D detailed geometries and 3D plasmas.
Acknowledgements:
M. Becoulet, CEA/IRFM, for the ELM density distributions.
PMLs
PMLs
PMLs
However most impact at ne,sep for this case
PMLs
ELM, N=1:9, 4MJ, 15MA/5.3T, No RMP
[M. Becoulet, IAEA 2020]
COMSOL (RAPLICASOL) modelling
ne
ne
Local midplane gas injection

## Slide 33: Outline
ITER ICRF system under the new ITER Research Plan (IRP).
ICRH scenarios.
Ion Cyclotron Wall Conditioning (ICWC).
Coupling and local gas injection modelling.
ICRF specific sputtering predictions under W-wall.
Full system RF modelling.
Antenna RF and mechanical design activities.
Antenna protections and arc detection.
Prototyping activities.
Conclusion and timeline.

## Slide 34: ICRF-specific sputtering in high-Z tokamaks
Continuous progress in increasing ICRF coupling & minimizing ICRF-specific sputtering, in particular with high Z wall: AUG & C-MOD.
Optimizations of both:
[*] “Radiation pattern” synthesis is common practice in antenna phased arrays; used for decades “outside nuclear fusion”. Now used in nuclear fusion (independently) to reduce ICRF-specific sputtering since first demonstration on AUG.
ATTIV, Local gas injection
-k0
+k0
3.8
9.6
1.3
Pcent/Ptot
<E//> [kV/m] @ surrounding PFC
[0;π;0;π]
Array antennas geometry, &
Excitation laws (incl. tapering or apodization) [*].

## Slide 35: International effort following new ITER baseline
WP1: Empirical extrapolation or “0D quantification” with IPP-Garching.
WP2: Modelling on SSWICH2D with CEA & support from IPP-Garching.
WP3: 3D RF sheath modelling (Dielectric Layer Method, implemented in COMSOL) followed by GITR modelling with ORNL with support from Lodestar Research Corporation.
WP4: 3D RF sheath modelling on Petra-M by PPPL.
4 Work-Packages launched in 2023 with international community (large effort):

## Slide 36
[V. Bobkov, et al., PSI 2024]
WP1 in a nutshell
Using HFSS with lossy dielectric as loading,.
Flat antenna models for AUG 3-strap and ITER.
Taken same boundary conditions, PFC shapes and radial position of straps.
Average <E||> over the whole height of calculation domain: conservative for ITER antenna.
Comparing AUG and ITER antennas:
Using results & typical values of sheath voltages from AUG 3-strap
 Extrapolation of results to ITER antenna.

## Slide 37
WP2 in a nutshell
Modelling using SSWICH-SW.
E// maps from TOPICA.
PML had to be adapted to propagative Slow Wave.
~30 runs, over large range of scenarios.
[L. Colas, et al., PSI 2024]
[L. Colas, et al., this conf.]

## Slide 38
Modelling results for reference 15 MA full field DT H-mode and conservative estimates:
Local gas injection
[0;π;π;0] in “Low 2010” conditions (Zone 1)
1 antenna
Vantenna [kV peak]
Pcoupled [MW]
Vantenna [kV peak]
Pcoupled [MW]
ΦW,wall = 5.5×1020 s-1
Zone 1
Zone 2
Low 2010
High 2010
High 2023
Coupling [MW] at 45 kV peak
[0;π;0;π]tapered in “High 2010” conditions (Zone 2)
Coupling [MW] at 45 kV peak
1 antenna
1 antenna
1 antenna
SSWICH
Empiric extrapolation,
10-20 MW, [0;π;0;π]tapered
Empiric extrapolation,
10-20 MW, [0;π;π;0]
Outcome from WP1 and WP2
WP1 & WP2 show compatibility with high power and low sputtering.
[W. Helou, et al., FEC 2023]

## Slide 39
No indication of propagative slow wave impacting near-fields and ICRF-specific sputtering in AUG.
COMSOL modelling results with Dielectric Layer Method:
|E|
Large, local fields, due resonance cones & propagative Slow Wave.
Notes:
The first indication shows that the resulting ICRF-specific sputtering could still be moderate.
Some WP3 results
[V. Bobkov, et al., PSI 2024]
Recent results from WEST are in-line with results from AUG.
[R. Diab, et al., this conf.]

## Slide 40
Some WP4 results
More distributed near fields.
Pinc = 10 MW.
nS=0 = 1 x 1017m-3.
Φz=[0;π;0;π].
Pcentral/Pouter
max(Vsh)
Impact of tapering less noticeable.

## Slide 41: IO strategy as per ICRF-specific in new IRP
WP1 & WP2
OR
WP3 & WP4
 Fully in-line with IO strategy:
ICRF-specific sputtering extrapolation is complex task.
ITER ICRF system is to be tested / experimentally validated at reduced power (10 MW) at SRO following which decision on upgrade to full-power (20 MW) will be taken.
OR
Other

## Slide 42: Outline
ITER ICRF system under the new ITER Research Plan (IRP).
ICRH scenarios.
Ion Cyclotron Wall Conditioning (ICWC).
Coupling and local gas injection modelling.
ICRF specific sputtering predictions under W-wall.
Full system RF modelling.
Antenna RF and mechanical design activities.
Antenna protections and arc detection.
Prototyping activities.
Conclusion and timeline.

## Slide 43: The electric circuit of the ITER ICRF system
Pre-match
(3-stub)
Phase-shifters
(based on hybrid couplers)
Decoupling / Beam-forming network
Main matching
Poloidal Splitters
(hybrid couplers) providing “load-resilience”
Antenna
Variety of tuning parameters: stubs, capacitors, sources’ power amplitudes & phases.
Many of these parameters can be real-time controlled.

## Slide 44: Static RF circuit simulations ongoing [1/2]
55MHz, [0;;0;], tapered, matched at Set7 (CASE4IPP)
Perfect matching achieved.
[K. Saito, ITER_D_B5ZEW4 v1.0]

## Slide 45: Static RF circuit simulations ongoing [2/2]
Notice load resilience (VSWR<2:1).
[K. Saito, ITER_D_B5ZEW4 v1.0]
55MHz, [0;;0;], tapered, mismatched, Set 1 (Low 2010)

## Slide 46: Matching algorithms development ongoing
[K. Saito, ITER_D_CHY9GQ v1.1]
Example of matching algorithm with:
Static stubs (ex. much less reduced risks of failure because of triboelectric aspects at the RF contacts).
Addition of matching capacitors in main matching.
Real-time controlled capacitors and frequency.

## Slide 47: Outline
ITER ICRF system under the new ITER Research Plan (IRP).
ICRH scenarios.
Ion Cyclotron Wall Conditioning (ICWC).
Coupling and local gas injection modelling.
ICRF specific sputtering predictions under W-wall.
Full system RF modelling.
Antenna RF and mechanical design activities.
Antenna protections and arc detection.
Prototyping activities.
Conclusion and timeline.

## Slide 48: Antenna RF calculation strategy
State of the art numerical tools and regular benchmarks (independent tools & expert users).
Antenna circuit portioned.
Component full-wave modelled.
Precise electric circuit extracted  voltage and current standing wave patterns extracted.
Power is raised until reaching Vmax=45 kV peak.
Compliance of |E| ensured for each component at Vmax.
Circuit optimized using iterations of hybrid circuit / full-wave calculations & interaction with multiphysics drivers (cooling, neutron shielding, space reservation, etc.).
[ITER_D_44M4QS v2.1]

## Slide 49
Click to play animation.
Plasma side
Front Window
Standing Wave Pattern along a triplet feeding line.
Coupled power for Vmax=45 kV peak.
FPJ
STS axis
Example of RF modelling results [1/2]
[ITER_D_44M4QS v2.1]
Notice: large VSWR, voltage nodes in vacuum.

## Slide 50
Example: RF loss densities from detailed full-wave modelling campain  Input for thermo-mechanical calculations (considered: impact of material tempearture, surface roughness, safety factor, etc.).
Service T-stubs inner conductors
Example of RF modelling results [2/2]
Integrated modelling covering: RF, electromechanical, thermomechanical, seismic, nuclear, 3D development & integration, etc.
[ITER_D_44M4QS v2.1]
log10(δ2P) [W/m2] at 55 MHz

## Slide 51: Outline
ITER ICRF system under the new ITER Research Plan (IRP).
ICRH scenarios.
Ion Cyclotron Wall Conditioning (ICWC).
Coupling and local gas injection modelling.
ICRF specific sputtering predictions under W-wall.
Full system RF modelling.
Antenna RF and mechanical design activities.
Antenna protections and arc detection.
Prototyping activities.
Conclusion and timeline.

## Slide 52
Example 1
Example 2
45 kV peak
ITER ICRF antennas designed considering:
Vmax= 45 kV peak [51ICs476-R] & |E| < 2-3 kV/mm (depending on orientation and location) [51ICs477-R] such as not to arc.
Protections by proper design: satisfying Vmax & Emax specifications
[ITER_D_44M4QS v2.1]
45 kV peak

## Slide 53
Corona rings
(protect triple-points)
IO designed Rear Window:
|E| for 45 kV peak
[ITER_D_5R8LUL v2.2]
Protections by proper design: corona rings for RF windows

## Slide 54
[51ICs151-R] All RF components that are exposed to high RF voltage shall be continuously monitored by redundant fast arc detection systems that are based on different concepts.
[51ICs153-R] In case of arcing the concerned subsystem shall deliver a fast signal to switch off the RF power feeding the whole concerned antenna subsystem, or, selectively, the RF power feeding the arcing subsubsystem(s)
[51ICs459-R] Automatic protection against arcing in antennas, power loads, transmission and matching systems and power sources shall be included in the design.
[51ICs483-R] The antennas shall be protected against internal malfunctions including arcing
[51ICs489-R] Equipment shall be provided within the antenna subsystem to ensure the detection of RF arcs, and to enable appropriate protective action to be taken by other subsystems before the onset of arc damage to the antenna.
[51ICs823-R] In case of an arc detected in a high RF power IC H&CD system component (source, main transmission line, matching circuit, antenna), the associated antenna sub-system shall automatically step back to the S4 state; the RF power shall be cut off in less than 10 µs (microseconds), in order to prevent a large amount of energy being delivered to the arc. The system shall automatically try to recover to the S5 state after an interruption time. The RF power interruption duration shall be adjustable (typically tens of ms), as well as the number of trips before definitive RF power cut off.
[ITER_D_28B33K - SRD-51 (ICH&CD) from DOORS]
ITER ICRF Antenna Arc Detection & Protection [1/5]

## Slide 55
# | Category | Detail | Comment
1 | Using RF signals at the operation frequency. | Vant,max measurements ( power limitation). | Extensive work with ERM under IO/20/CT/4300002178.
 |  | VSWR or ¦Γ¦. | 
 |  | arg(Γ) and phase jumps. | 
 |  | Balance of line voltages, &/or currents, &/or Z. | 
 |  | Mix of RF signals (AWACS-like, voltage balances, etc.). | 
 |  | Scattering Matrix Arc Detection (SMAD). | 
2 | Plug/port cavity fields monitoring. |  | Extensive work with ERM under IO/20/CT/4300002178
3 | Optical Arc Detection |  | 
Likely only for the antenna prototype
(no probes in vacuum for the full antenna).
Likely only during installation of antenna in torus.
In vacuum: likely only for the antenna prototype module.
[2024_11_27-28 _ ITER ICRF Antenna Arc Detection and Protection Workshop 1, CQ2CVF]
ITER ICRF Antenna Arc Detection & Protection [2/5]
[F. Louche, et al., this conf.]
[A. Krivska, et al. this conf.]

## Slide 56
Proof of principle for ITER ICRF RAAD by:
Modelling  DONE.
Implementation and validation tests of a prototype RAAD module  Ongoing.
# | Category | Detail | Comment
4 | Broadband Tx / Rx: active RADAR. | RADAR arc & impairment detection & localization (RAAD). | Extensive work with Politecnico di Torino under IO/24/CT/4300003010.
[S. Porporato, et al., this conf.]
[D. Milanesio, et al., this conf.]
Work with Politecnico di Torino:
Ongoing: implementation of framework for tests on AUG in 2026.
[A] RAAD is able to detect arcs in less than 5 μs.
[B] RAAD shall protect the windows, and detect arcs at the low voltage regions in the antennas.
[C] RAAD is able to discriminate arcs from other events.
Proof of principle
[2024_11_27-28 _ ITER ICRF Antenna Arc Detection and Protection Workshop 1, CQ2CVF]
ITER ICRF Antenna Arc Detection & Protection [3/5]

## Slide 57
# | Category | Detail | Comment
5 | Broadband Rx: “passive” RADAR. | Sub (& Sup) Harmonic Arc Detection (SSHAD). | Feedback from: CEA-IRFM, AUG, JET. Politecnico di Torino under IO/24/CT/4300003010.
At the operation frequency, the generators and antennas are tuned; but they are mismatched at all other frequencies.
The system acts as a cavity with its own resonance frequencies FR,m.
Arc: fast transient event  Broad spectrum  Excites cavity at FR,m.
SHAD: measures ~comb pattern resulting from an arc.
Work ongoing with Politecnico di Torino for developing intelligent SSHAD to discriminates arcs from other events.
…
α1
α2
α3
α4
α5
α6
α7
α8
Ongoing: implementation of framework for tests on AUG in 2026.
[2024_11_27-28 _ ITER ICRF Antenna Arc Detection and Protection Workshop 1, CQ2CVF]
ITER ICRF Antenna Arc Detection & Protection [4/5]

## Slide 58
# | Category | Detail | Comment
6 | Stray microwave radiation sensing. | Stray EC sensing (170 GHz). | Extensive work with Politecnico di Torino under IO/24/CT/4300003010
Ongoing: implementation of framework for tests on AUG in 2026.
Stray EC can penetrate in the ITER ICRF system and deposit power in the ceramics  Needs to be detected.
[P. Lamalle, ITER_D_5RUPCN]
Work with Politecnico di Torino:
FEKO
Experiments
Parametric scans
(noise floor: ~-92 dB)
[2024_11_27-28 _ ITER ICRF Antenna Arc Detection and Protection Workshop 1, CQ2CVF]
ITER ICRF Antenna Arc Detection & Protection [5/5]

## Slide 59: Outline
ITER ICRF system under the new ITER Research Plan (IRP).
ICRH scenarios.
Ion Cyclotron Wall Conditioning (ICWC).
Coupling and local gas injection modelling.
ICRF specific sputtering predictions under W-wall.
Full system RF modelling.
Antenna RF and mechanical design activities.
Antenna protections and arc detection.
Prototyping activities.
Conclusion and timeline.

## Slide 60: Prototype Antenna Module (PAM) in Port Plug Test Facility (PPTF)
RF source
(120 kW CW)
PPTF
Validate manufacturing, assembly, etc.
Lower power characterizations.
High CW power validation tests under maximal RF voltages and currents.
Retro-engineering if needed.
Tests at ~41 MHz and~54 MHz.
Tests of antenna protections.
Tests for Instrumentation & Control..
Pre-match

## Slide 61: RF windows test articles
RF windows (Front Window and Rear Windows) progressing. Contracts with ASIPP, PMB and Vitzrotech.
Vmax
Imax
Example for ASIPP windows: VNA tests for prototype RW Test Article, and Hipot tests.
Conservative
(1 atm air)
[J.-M. Bernard, et al., this conf.]
Next steps, tests at high voltage and high current, in CW.
  Modular design of the resonator:
  Vmax and Imax.
  FW & RW.

## Slide 62: RAAD, SSHAD and EC sensing + tests on AUG
WR6.5 Sensing Aperture
RAAD:
EC sensing:

## Slide 63: Outline
ITER ICRF system under the new ITER Research Plan (IRP).
ICRH scenarios.
Ion Cyclotron Wall Conditioning (ICWC).
Coupling and local gas injection modelling.
ICRF specific sputtering predictions under W-wall.
Full system RF modelling.
Antenna RF and mechanical design activities.
Antenna protections and arc detection.
Prototyping activities.
Conclusion and timeline.

## Slide 64: Conclusion and timeline
ITER ICRF CW high power RF system overviewed.
Large & complex system.
Good progress on all sub-systems. Design, R&D and prototyping ongoing.
Ready for high power operation in the tokamak
Delivery
SAT in PPTF
Installation in Port Cell
Baking
Delivery + Antenna FDR
RF tests in PPTF
Delivery of windows
+ Resonator commissioning
RF tests

## Slide 65: Related contributions at RFPPC2025
Authors | Contribution
E. Lerche, et al. | Real-time estimates of the ICRF single-pass absorption for ITER.
S. Porporato, et al., | Radar arc and impairment detection and localization for the ITER ICRF antenna.
D. Milanesio, et al., | Full-wave modeling of arcs within the ITER ICRF antenna for usage in the simulations and design of the RADAR Arc Detection system.
F. Louche, et al., | Progress in the analysis of the cavity resonances in the ITER ICRF antenna port plug.
A. Krivska, et al., | Calculation of the magnetic field and its modal analysis in the port plug cavity of the ITER antenna.
L. Colas, et al., | Damping RF waves with low reflection in simulations of slab or curved magnetized plasma: parametrization, verification and implementation of Bermudez Perfectly Matched Layers.
R. Diab, et al., | Direct Measurement of ICRF-Enhanced Plasma Potentials Using Reciprocating Emissive Probes on the WEST tokamak.
J.-M. Bernard, et al., | Development of an actively cooled radio-frequency test bench for the ITER ICRF windows.
M. Schneider, et al., | Operation of the Electron Cyclotron system in the ITER new baseline.